## Slide 1: X Ray Diffraction

## Slide 2: X Ray diffraction
X-ray diffraction analysis (XRD) is a technique used in materials science to determine the crystallographic structure of a material.
XRD works by irradiating a material with incident X-rays and then measuring the intensities and scattering angles of the X-rays that leave the material.
A primary use of XRD analysis is the identification of materials based on their diffraction pattern.

## Slide 3: How does it Work?
Crystal atoms scatter incident X-rays, primarily through interaction with the atoms’ electrons. This phenomenon is known as elastic scattering; the electron is known as the scatterer.
A regular array of scatterers produces a regular array of spherical waves.
In the majority of directions, these waves cancel each other out through destructive interference, however, they add constructively in a few specific directions, as determined by Bragg’s law:
2dsinθ = nλ
  Where d is the spacing between diffracting planes,
  Θ is the incident angle,
  n is an integer,
  λ is the beam wavelength.
The specific directions appear as spots on the diffraction pattern called reflections.

## Slide 4: Principle
X-ray diffraction is based on constructive interference of monochromatic X-rays and a crystalline sample.
These X-rays are generated by a cathode ray tube, filtered to produce monochromatic radiation, collimated to concentrate, and directed toward the sample.
These diffracted X-rays are then detected, processed and counted.
https://www.youtube.com/watch?v=QHMzFUo0NL8

## Slide 5: Strengths and Limitations
Strengths
Powerful and rapid (< 20 min) technique for identification of an unknown mineral
In most cases, it provides an unambiguous mineral determination
Minimal sample preparation is required
XRD units are widely available
Data interpretation is relatively straight forward
Limitations
Homogeneous and single phase material is best for identification of an unknown
Must have access to a standard reference file of inorganic compounds (d-spacings, hkls)
Requires tenths of a gram of material which must be ground into a powder
For mixed materials, detection limit is ~ 2% of sample
For unit cell determinations, indexing of patterns for non-isometric crystal systems is complicated
Peak overlay may occur and worsens for high angle 'reflections'