## Slide 1: Distillation
Dr. Garima Joshi
Assistant Professor
Department of Pharmaceutical Sciences, MLSU
III Sem, Unit operation

## Slide 2: General Introduction
Distillation is an unit operation which involves separation of a vaporizable component from a multi-component system and subsequent condensation of vapours.
It is a process of separating the component substances from a liquid mixture by selective evaporation and condensation.
It is defined as the separation of the components of a liquid mixture by a process involving vaporization and subsequent condensation at another place.

## Slide 3: Applications/ need
Separation of volatile oils- cloves(Eugenol comprises 72-90%, Vanilin, acetyl eugenol).
Separation of drugs obtained from plant and animal sources- Vit. A from fish liver oil.
Purification of organic solvents-absolute alcohol (100%).
Purification of drugs obtained from chemical process.
Manufacture of official preparations -sprit of nitrous ether, sprit of ammonia, D.water and water for inj.
Quality control methods- Alcohol content in elixir(4-40%).
Refining of petroleum products- Petroleum ether 60,80.
Recovery of solvents- synthesis.

## Slide 4: TERMINOLOGY
Ideal Solution (Perfect solution)
Ideal solution is defined as the one in which there is no change in the properties of components other than dilution, when they mixed to form a solution.
Property of ideal solution
Total volume of solution is equal to sum of volumes of each component .No heat absorbed and No heat evolved.
No Chemical reaction in-between. Final volume of solution represents additive property of individual components.
Follow Raoult’s law .

## Slide 5: Real solution
Real Solution
Most system shows varying degree of deviation from raoult’s law, depending on nature of liquids and temperature. These solution are known as real solution.
Property of Real solution
Heat may absorbed or evolved
Chemical reaction occurs in-between
Final volume of solution represents additive property of individual components
Don’t Follow Raoult’s law
Example  Carbon tetra-chloride + Cyclohexane  Choroform + Acetone

## Slide 6: Volatility
The volatility of any substance in solution may be defined as the equilibrium partial pressure of substance in vapour phase divided by the mole fraction of substance in the solution.
For example, a substance A in a liquid mixture has partial pressure PA and its concentration in the mixture is XA on mole fraction scale.
Partial vapour pressure of A Volatility of component A, = Mole fraction XA of A in solution vA = PA/XA
The volatility of a material in the pure state is equal to the vapour pressure of the material.

## Slide 7: Relative Volatility
Consider a liquid mixture containing two component A and B, In such case, the volatility of one component is expressed in terms of second as below,
Relative Volatility ( ) = Volatility of component A (VA) ____________________
Volatility of component B (VB)
= VA/VB

## Slide 8: Vapour Pressure
Vapor pressure - It is defined as the pressure exerted by a vapor in thermodynamic equilibrium with its condensed phases (solid or liquid) at a given temperature in a closed system.
The equilibrium vapor pressure is an indication of a liquid's evaporation rate.