## Slide 1: Optical Mineralogy
LECTURE -7, M.Sc. ( Geology) I Semester
NIRANJAN MOHANTY
DEPARTMENT OF GEOLOGY,
MLS UNIVERSITY
UDAIPUR-313001 (RAJASTHAN)
E-mail: niranjan@mlsu.ac.in

## Slide 2: Path Differences In Crystals
Waves entering an anisotropic crystal will generally experience two indices of refraction in two perpendicular directions
Even plane-polarized radiation will be split into the Ordinary (O) and Extraordinary (E) vibrating 

## Slide 3: Retardation
Path differences upon passing through a crystal are called retardation (of the slower ray relative to the faster)
Δ = λ in this case
Notes: Diagram: http://www.brocku.ca/earthsciences/people/gfinn/optical/retard6.gif

## Slide 4: Accessory Plates
Quartz sensitive tint, gypsum plate, 1st order red has Δ = 550 nm
Mica or quarter-wave plate has Δ = 150 nm
Quartz wedge has variable Δ
Generally, the slow direction is indicated on the plate (N) – the fast direction (n) is unmarked, but is perpendicular

## Slide 5: Accessory Plate Photo
Left to right: Quarter wave plate; full wave sensitive tint plate; quartz wedge
Viewed in crossed-nicols
Notes: Image: http://www.msm.cam.ac.uk/doitpoms/tlplib/optical-microscopy/plates.php

## Slide 6: Quartz Sensitive Tint Plate
Usually made of gypsum, mica, or quartz
Mineral is cut parallel to the optic axis of the crystal, to such a thickness that the O-rays and E-rays for green light (l = 540 nm) are out of phase by exactly one wavelength
The analyzer therefore extinguishes green light, but permits other wavelengths to pass through to some extent
When using white light this causes the field of view to appear red (white light minus green light)
Isotropic, non-birefringent materials also appear red
Notes: Source: http://www.msm.cam.ac.uk/doitpoms/tlplib/optical-microscopy/plates.php

## Slide 7: Quarter-wave Plate
Made form a flake of mica that is cleaved to such a thickness that the O-rays and E-rays emerge a quarter of a wavelength out of phase
This corresponds to a pale grey interference color
This plate is especially useful for examining specimens showing bright interference colors, because they are moved only a short distance along the scale
The plate can be used to enhance the contrast between regions of the specimen

## Slide 8: Quartz Wedge Plate
The quartz wedge is cut so that it varies in thickness from about 0.01 mm to about 0.08 mm and covers several orders of retardation colors
As the wedge is inserted into the slot in the microscope it produces progressively higher retardations, and the position at which complete extinction occurs is noted
Michel Levy produced a color chart which plots the thickness of an isotropic specimen, its birefringence and its retardation in nanometers
Once two of these variables is known, the third can be easily determined

## Slide 9: Calculating Δ
Δ = c (TN - Tn)
Where
  TN = time for the slow wave to pass through the xtal
  Tn = time for the fast wave to pass through the xtal
If the thickness of the crystal is t, then:
  cN = t/TN and cn = t/Tn

## Slide 10: Calculating Δ continued
Δ = c (t/cN – t/cn) = t (c/cN – c/cn)
But N = c/cN and n = c/cn
Therefore, Δ = t(N –n)

## Slide 11: Sample Calculation
For quartz, N = 1.553 and n = 1.544
Thickness of a standard section = 30 microns = 0.03 mm
Δ= (1.553 – 1.544) x 0.03mm = 2.7 x 10-4 mm = 270 nm
For calcite, N = 1.658 and n = 1.486
Δ = (1.658 – 1.486) (0.03) = (0.172) (0.03) = 5.160 x 10-3 mm = 5160 nm

## Slide 12: Transmission of Light
Crystal viewed 45 ̊ off extinction (where interference colors are brightest) with nicols crossed
  L = 100 sin2 Δ/λ 180 ̊
    (L = percent transmission)
For parallel nicols
  L = 100 cos2 Δ/λ 180 ̊

## Slide 13: Plot of Transmission vs. λ
Note: Curves labeled 10 λ, 9λ, etc. should say 10 Δ/λ, 9 Δ/λ, etc.
Solid line, Δ = 4000 nm
Dashed line, Δ = 200 nm

## Slide 14: Use of Accessory plates
Anisotropic crystals will show their most intense, or brightest, interference colors at a position 45 ̊ off extinction
When an accessory plate is inserted into the light path, with the fast direction of the crystal and accessory plate parallel, the retardations produced by each will add

## Slide 15: Example of Addition
If the crystal Δ= 250nm (1 ̊ yellow) and the accessory Δ = 550nm the total retardation will be 800nm (2 ̊ green)
The accessory will always raise the retardation color to a higher retardation if the fast directions are parallel

## Slide 16: Michael Levy Color Chart
As retardation increases, we see colors in order from blue to red
After one set of colors, the pattern repeats, so we get first-order, second-order, etc.

## Slide 17: Subtraction
If the slow direction of the crystal is parallel to the fast direction of the accessory plate, we will see a retardation color equal to the absolute value of the difference of their Δ values

## Slide 18: Example of Subtraction - 1
Δ crystal = 300nm (1 ̊ yellow)
Δ accessory = 150nm
300 – 150  = 150 (1 ̊ gray)

## Slide 19: Example of Subtraction - 2
Δ crystal = 200nm (1 ̊ gray)
Δ accessory = 550nm
200 – 550 mm = 350nm (1 ̊ yellow)
In this case the subtraction has enhanced the color!
However, if we rotate the stage 90 degrees, so that the fast directions are parallel, the addition process will occur and Δ total = 550 + 200 = 750 (2 ̊ blue - green)

## Slide 20: Relation Between Addition and Subtraction
Thus, the addition process always produces a higher color than the subtraction process

## Slide 21: Sign of Elongation
Crystals which are elongated are said to be length - slow if the slow direction of the crystal is parallel to the long direction of the crystal
Elongated crystals are length – fast if the fast direction of the crystal is parallel to the long direction of the crystal

## Slide 22: Orthoscopic Observation
Normal use of a microscope is on the orthoscopic mode – the light from the source of illumination is parallel, or as nearly parallel as is possible
Notes: Diagram: http://www3.uakron.edu/geology/friberg/optical/lecnotes/lec10.html

## Slide 23: Conoscopic Observation
An alternate way of using the microscope involves conoscopic illumination
In this case the condensing lens is moved closer to the objective lens, and the illumination occurs along the surface of a cone
Notes: Diagram: http://www3.uakron.edu/geology/friberg/optical/lecnotes/lec10.html

## Slide 24: Objective Lenses
Most petrographic microscopes have at least three interchangeable objective lenses of different magnifications and numerical apertures
Aperture is the opening, or width, of a lens

## Slide 25: Angular Aperture
Aperture may be measured in terms of the angular aperture
Numerical Aperture = n sin μ
  Where n is the lowest index of refraction of any medium filling the gap between the objective and the thin section
  Generally this medium will be air (dry case) or an immersion oil

## Slide 26: Angular Aperture Diagram
Angular aperture is the size of the cone of light that the lens can accept (30° or 118°)

## Slide 27: Maximum N.A. Value
Sin function has a maximum value of 1.0, so N.A. values cannot exceed 1.0 for the dry case
Oil immersion lens are available with magnification of 100x and N.A. values of 1.30

## Slide 28: Importance of N.A.
Orthoscopic – determines the resolution (smallest detail can be distinguished) of a microscope
  The higher the N.A, the better the resolution
Conoscopic – determines how much of an interference figure can be seen
  The larger the N.A. value, the more of the figure you can see
  This makes identification easier

## Slide 29: Oil Immersion Lens
To use the very high power, larger N.A. lens it is necessary to use immersion oil with n >1.3
The condensing lens must have an N.A. comparable with the objective lens

## Slide 30: Properties of Immersion Oils
Oils used are generally organic oils of various types
Oils higher than 1.8 often contain poly-chlorinated biphenyls (P.C.B.’s) and must be used with great caution
P.C.B.'s have been shown to be powerful carcinogens

## Slide 31: Depth of Focus
The depth of focus is the range over which objects are in focus
It is an inverse function of N.A.
Low power lens are typically easy to focus
High power lens have a very small (10 microns for a 40-45x objective) depth of focus

## Slide 32: Extinction Angle
Non-isotropic substances will go into extinction (show 1 ̊ black interference colors) four times as the stage is rotated in a full circle, or once every ninety degrees
Frequently a grain will have a prominent linear feature which can serve as a reference line
Such linear features are generally either crystal faces or the lines of intersection of cleavage planes with the crystal plate surface
The latter are called cleavage traces

## Slide 33: Parallel Extinction
The crystal direction is parallel to the cross-hair at extinction
τ = 0 ̊
Also called straight extinction
Not possible in triclinic crystals

## Slide 34: Symmetric Extinction
When a crystal shows two crystal directions (such as cleavage traces) the extinction position may bisect the angle between the crystal directions
τ ≠ 0 ̊
Not possible in triclinic crystals

## Slide 35: Inclined Extinction
A single crystal direction will not be parallel to a crosshair at extinction
This can occur only in biaxial crystals
τ ≠ 0 ̊

## Slide 36: Undulatory Extinction
Extinction will look like a wave passing across a crystal as the stage is rotated
Often results from deformation of a crystal
Quartz frequently shows undulatory extinction

## Slide 37: Natural Color
Many minerals are transparent at the standard thickness of a thin section (30 microns)
Absence of color is not reported
Presence of color should be reported as natural color, when viewed in plane polarized light

## Slide 38: Absorption
Minerals displaying natural color may change the intensity of their color as the stage is rotated
Example: A light green color may become darker green
Such a change can be noted as a change in absorption

## Slide 39: Pleochroism
Many colored anisotropic minerals, viewed in PP light, will show a change in color as the stage is rotated
The change in color is called diachroism or pleochroism (literally meaning many colors)

## Slide 40: Describing Pleochroism
For pleochroic minerals the observed color range should be reported
For example:
  Inky blue to dark brown
  Colorless to light yellowish-green