## Slide 1
DOWNSTREAM
PROCESSING

## Slide 2
WHAT IS DOWNSTREAM
PROCESSING ???
The various process used for actual Recovery and
purification of biosynthetic products from a
fermentation or any other industrial process together
constitute a downstream processing.
4

## Slide 3
WHAT ARE THOSE PROCESSES ???
Removal of
insoluble
Isolation or
extraction of
product
concentration of
product
Packaging of
product

## Slide 4
WHAT ARE THE CLASSES OF
PRODUCT OBTAINED???
Cell itself
• Bakers yeast
• Bio-fertilizers
Extracellular type
• Antibiotics
• Alcohol
Intracellular type
• Enzymes
• Vitamins

## Slide 5
IF THE PRODUCT IS THE CELL ITSELF
???
Separation of particles
• Filtration
• Centrifugation
• Flocculation and floatation
Cooling and
packaging
-

## Slide 6
IF THE PRODUCT IS EXCRETED OUTSIDE
THE CELL ??
• Centrifugation or filtration
• Flocculation and floatation
Separation of
Particles
• Liquid-liquid extraction
• Whole broth extraction
• Aqueous Multiphase Extraction
Extraction
• Chromatographic techniques
• Evaporation process
• Crystallization
• Adsorption
Concentration

## Slide 7
IF THE PRODUCT IS INTRACELLULAR ???
• Filtration
• Centrifugation
• Flocculation
and floatation
Separation
of particles
• Mechanical
cell disruption
• Drying
• Lysis
Disintegration
of cells
• Liquid-liquid
extraction
• Whole broth
extraction
• Aqueous
multiphase
extraction
Extraction
• Evaporation
• Membrane
filtration
• Chromatography
techniques
• Adsorption
Concentration

## Slide 8
TECNIQUNIES INVOLVED IN DOWNSTREAM PROCESSING
1. Filtration
filamentous fungi
filamentous bacteria
Yeast

## Slide 9
18-03-2017
Basic Science H.O.T.
13
Surface
filters
Filtration on
the basis of
pore size of
the
membrane.
Cross flow
filters
Filtration on
the basis of
pore size but
pores are not
clogged due
to tangential
flow of
particles
Rotatory
flow filters
Filtration due
to sucking of
liquid by
vacuum
when filter
drum is
rotated in the
slurry.
Depth filters
Uses a porous
filtration
medium to
Retain particles
through out
the medium
rather than just on
Centrifugal
filters
Filtration by
rapidly
rotating
slurry, so
solids are
retained on
porous screen
and liquid
filter out

## Slide 10
2. CENTRIFUGATION
•Works on
sedimentation
principle
The centripetal
acceleration
causes
denser
substances and
particles to
move outward
and less dense
are displaced
and move to
the centre
14

## Slide 11
3. FLOCCULATION AND FLOATATION
•Flocculation is the process by which
individual particles aggregate to form
a clump
•Due to addition of clarifying agent
Floatation is the process of
separation of particles based on
relative buoyancy of particles
Froth flotation
Dissolve air flotation
Induced gas flotation
15

## Slide 12
4. CELL DISRUPTION
Ultra
sound
Bead mill
Homogenisers
•Drying
Lysis by osmotic
shock
Freezing
Lytic enzymes
Mechanical cell lysis
Non-mechanical cell lysis

## Slide 13
LIQUID SHEAR
SOLID SHEAR
BLENDERS
FREEZE
THAWING
ULTRA
SONICATION

## Slide 14
1.HOMOGENIZERS:

Pumps the slurry through a
restricted orifice valve.

Uses high pressure up to 1500 bar
followed by instant expansion
through a special exiting nozzle.
Cell disruption is accomplished by High liquid shear in the orifice and
Sudden pressure drop upon discharge

## Slide 15
2.Ball mill/Bead mill:

Devices used to rapidly grind materials to colloidal fineness
(1 micron or below)

Grinding is carried out with steel or
ceramic balls within the cylinder.

Cells are agitated with small abrasive
particles

Cells break due to shear forces
3.BLENDERS:
Simple method used to disrupt the cells in case of weak cell wall.
High speed mixing is employed.

## Slide 16
4.FREEZE THAWING:
Freezing and thawing of microbial cell will cause formation of ice
crystals and repeated freeze thawing will lead to subsequent disruption
of cell.
Slow process with limited release of cell contents.
5.Ultrasonication:
High frequency vibration (20 kHz) transported through a metallic
tip to an concentrated cellular suspension
Leads to creation of cavities, thereby shock
Disadvantages
waves disrupt the cells.
Method is costly and effective in small scale.
Cells break completely leading to release of all cellular materials.

## Slide 17
DETERGENTS
CHAOTROPIC
AGENTS
OSMOTIC
SHOCK
ALKALI
TREATMENT
ENZYME
TREATMENT

## Slide 18
1.Detergents:
Cause damage to lipoproteins of cell wall of microorganisms.
Compounds used are sodium lauryl sulphate,sodium dodecyl sulphate,
triton X-100,phenyl ethyl alcohol, dimethyl sulphoxide, benzene,
methanol, chloroform etc.
Triton X-100 with guanidine-HCL is widely and effectively used for
release of cellular proteins.
2.Alkali treatment:
Used for hydrolysis of microbial cell wall.
Provided that the desired product will tolerate a pH of 11.5 to 12.5
for 20 to 30 minutes.

## Slide 19
3.Osmotic shock:
Caused by sudden change in salt concentration.
Proved to be a successful tech’ for extraction of luciferase from
Photobacterium fisheri
.
High salt concentration causes cell lysis & low salt concentration causes
over accumulation of water inside the cell leading to bursting of cell.
4.Enzyme treatment:
Used to permeabilize cells to release the cell
contents.
Enzymes used include, glucanase, protease,
mannase, lysozyme etc.
Expensive method and presence of enzyme may further complicate
purification processes.

## Slide 20
5. EXTRACTION OF PRODUCT
•Liquid-liquid extraction
•Separation of compound
based on there relative
solubility's in two different
immiscible liquids
Whole broth
Both cells and broth are
extracted together
Aqueous multiphase extraction
Enzymes are extracted in
aqueous polyethylene glycol-
dextran mixture, which form
separate phases

## Slide 21
6. CONCENTRATION
•Evaporation
Membrane
filtration
Ion exchange
chromatography
Adsorption
resins

## Slide 22
7. PURIFICATION
•Crystallization
•Impure substances are
dissolved in solvent to reach
saturated stage at higher
temperature which is then
cooled to form pure crystals
•Antibiotics like penicillin G,
Chromatographic
techniques

## Slide 23
Paper chromatography
Thin layer chromatography
Column chromatography
Ion exchange chromatography
Affinity chromatography
High performance liquid
chromatography
Reversed phase high
performance liquid
chromatography
Gas chromatography-mass
spectrometry
Gel filtration –
chromatography/ size exclusion
chromatography
Types of
chromatography

## Slide 24
PAPER CHROMATOGRAPHY
18-03-2017
Basic Science H.O.T.
22
Stationary
phase
Solid
(paper)
Filter
Paper
Filter
Towel
Mobile phase
Organic
solvent
Water,
rubbing
alcohol
Characteristics
Based on
polarity
And Size
Amino
Acids
Mechanism
If molecule to
be separated
are more
attracted to
stationary
phase then it
will move
slowly and
vise versa.
Advantage
1.Cheaper
2. Both
organic and
inorganic
compounds
can be
identified
Disadvantage
1. Large
quantity of
sample
cannot be
applied
2.complex
mixture
cannot be
separated
3. Less
accurate

## Slide 25
18-03-2017
Basic Science H.O.T.
23

## Slide 26
THIN LAYER CHROMATOGRAPHY
18-03-2017
Basic Science H.O.T.
24
Stationary
phase
Solid
Glass slide
with silica
gel,
Aluminum
oxide
Mobile
phase
Organic
solvent
Ethanol,
water,
hexane,
pentane
Characteristics
Attraction
of
compound
to solid or
liquid
phase
Mechanism
- Based on
retention
factor Rf
- Higher the
Rf higher the
rate with
which
product has
travelled
Advantages
- Simple
- Cheap
- Easy
recovery of
product
Disadvantages
- Plate length
limited so
separation up
to limited
length
- Sample
affected by
Humidity and
Temperature

## Slide 27
18-03-2017
Basic Science H.O.T.
25

## Slide 28
COLUMN CHROMATOGRAPHY
18-03-2017
Basic Science H.O.T.
26
Stationary
phase
Silica gel
Alumina
Mobile
phase
Solvent
according to
stationary
phase
Organic
solvents
Characteristics
Differential
adsorption
of substance
by
adsorbent or
relative
affinity
Mechanism
Based on
retention
factor Rf
- Higher the
Rf higher the
rate with
which
product has
travelled
Advantages
- Low cost
-Disposability
of stationary
phase so less
cross
contaminatio
n
Disadvantages
-Time
consuming
- Low
separation
power
-Irreproducible
result

## Slide 29
18-03-2017
Basic Science H.O.T.
27

## Slide 30
GAS CHROMATOGRAPHY MS
-
Stationary
phase
Volatile
liquid
Mobile
phase
Gas(carrier)
Inert gas
(He, Ar,
Ne)
Characteristics
volatility
Polarity
Mechanism
Separation
due to
equilibrium
established
between the
solutes and
stationary
phase
Advantages
-Fast
-Sensitive
-High quality
product
obtained
-More
resolution
Disadvantages
-Apply to only
volatile
compound
-Performed at
higher
temperature so
thermally liable
compounds
cannot be
analyzed
-Detectors used
are destructive

## Slide 31
18-03-2017
Basic Science H.O.T.
29
Retention time
Time taken by compound
to be detected
Nature of stationary phase
Solubility of gas in solid phase
Length of column
Temperature of column
Flow rate of mobile phase

## Slide 32
MASS SPECTROMETRY
18-03-2017
Basic Science H.O.T.
31

## Slide 33
18-03-2017
Basic Science H.O.T.
33

## Slide 34
18-03-2017
Basic Science H.O.T.
35

## Slide 35
18-03-2017
Basic Science H.O.T.
36

## Slide 36
ADVANTAGES AND DISADVANTAGES OF
HPLC
18-03-2017
Basic Science H.O.T.
38
ADVANTAGES
•
Can be applied to any compound soluble in liquid
phase ex. AA, Lipids, Carbohydrates
•
Performed at room temperature so thermally
compounds can analyzed
•
More flexible
•
detectors can be reused i.e. they are non destructive
Disadvantages
• Slower technique than GC
•
Lower resolution when compared to GC.

## Slide 37
ION-EXCHANGE CHROMATOGRAPHY
18-03-2017
Basic Science H.O.T.
39
Stationary
phase
Solid
Cellulose,
Agarose
Mobile phase
liquid
characteristics
polarity
Solubility
Mechanism
Charged molecules
attaches to the
oppositely charged
stationary phase as
a result the
molecules are
separated and the
molecule of interest
can be eluted by
adding another
compound which
has more affinity
for those charged
sites
Advantages
More matrix
tolerance
Sensitive
High quality
product
obtained
Disadvantages
Expensive
less
Reproducible

## Slide 38
18-03-2017
Basic Science H.O.T.
40

## Slide 39
18-03-2017
Basic Science H.O.T.
41

## Slide 40
GEL- FILTERATION/ MOLECULAR
EXCLUSION CHROMATOGRAPHY
18-03-2017
Basic Science H.O.T.
42
Stationary
phase
Beads with
holes
hydrocarbon
like dextran
Mobile phase
Liquid
Organic
solvent
characteristics
Size
Mechanism
Based on size
proteins can
pass through
the holes in
beads as a
result pass the
column first
and vice versa
Advantages
Good
separation
Biological
activity of
particles
protected
Less and
defined time
No sample
loss
Disadvantages
Molecules
with exact
same size and
weight cannot
be separated

## Slide 41
18-03-2017
Basic Science H.O.T.
43

## Slide 42
SDS- PAGE
•Proteins
are purified
• setup
similar to
gel
electrophore
sis
Based
on size
Forces
applied
Frictional
force and
Electric
force
(Gravitation
al force can
be
neglected)
Velocity
depends on
Electric
field,
Charge on
molecule
and
coefficient
of fricition
•Polyacramide
gel is
unreactive
It has many
pores to allow
proteins to pass
SDS anions and
Beta
mercaptoethanol
denatures the
protein by
attaching to side
chains.
So net charge
becomes
negative on
protein
18-03-2017
Basic Science H.O.T.
44

## Slide 43
18-03-2017
Basic Science H.O.T.
45

## Slide 44
8. PACKING
•Drying
Spray
Vaccum
Freeze
drying

## Slide 45
18-03-2017
Basic Science H.O.T.
59